## Slide 1: CubeSat CDR Format
November 22, 2024

## Slide 2: CDR Charts
Purpose of CDR is to certify the final design meets all design criteria and to get approval to release drawings to start ordering parts and material
Always put chart number on all charts
Create a chart the clearly identifies all the design requirements and how your design meets each requirement in a table format
  Column one: design requirement
  Column two: how design requirement is satisfied
Clearly indicate all final design details, both mechanically and electrically
Final design should be in Onshape
Create a chart that shows that shows the full completed final design Onshape assembly
  Then clearly identify all parts of your subassembly, by pointing to each part or show in an exploded view
Chart number 

## Slide 3: CDR Charts
Create a chart showing clearly how your subassembly is assembled
  Clearly indicate how the subassembly is attached both mechanically and electronically
  Indicate any welds and the number and size of all bolts
  If have heater clearly indicate the heater that will be used and how it will be attached mechanically and electrically. Indicate heater voltage, current, and power.
Create a chart that shows how boards can be replaced by disasassembling
Create a chart that has a table listing your bill of materials for your all parts of your assembly, including every electronic component, heater, etc.
  Make sure you know who will order bolts, heaters – your team or structure team
  Make sure you clearly indicate how many of each part will be procured
  For example, will your assembly be tested as a subassembly to verify thermal and vibration margins to reduce wear on flight assembly? Then need to do test on prototype hardware
    Probably want to do this with attitude control system, at a minimum

## Slide 4: CDR Charts
Clearly show each electronic board with all the all the components and how those components are attached to the board
  Clearly show how the board is attached mechanically and electrically
  Clearly indicate the type of connector (how many pins) and how the connector is mechanically attached
Create a table for each board that shows each electronic component spec sheet values for power, voltage, current, temperature allowables vs CubeSat orbit maximum power, voltage, current, and temperatures
  Need to clearly demonstrate derating margin
  Table will show for each component, the type of component, the allowables, and the operational values

## Slide 5: CDR Charts
Clearly indicate the total weight of each subassembly
Create a software chart indicating how the software for your subsystem will work
  Clearly indicate the software that comes with your subsystem and the software that will be needed to interface with your subsystem
  Clearly indicate expected lines of code, the software that will be used, and who will write the code
Create charts that clearly indicate the type of testing that you expect to perform on each subsystem to verify subsystem performance meets subsystem design criteria
  Indicate any test equipment that will be needed and the cost of the test equipment

## Slide 6: CDR Charts
Create a chart that indicates tooling needed and the cost of tooling
Show Gannt chart with one week as time increment and when scroll down make sure that the weeks are still shown on the top and the tasks are still shown on the left side
  Clearly show the entire schedule to completion, including such significant milestones as assembly, test readiness review, tests, integration into CubeSat, software completion
  Clearly indicate the critical path (which will be software completion and verification for communications, command, and controls subsystems)
Clearly indicate the cost of each subsystem

## Slide 7: CDR Charts For Structures group
Indicate expected strength margins for as many parts as possible for random vibration loads in a table
  Table should show part, material strengths, peak 3 sigma stress, and margin of safety using yield and ultimate strengths
Clearly identify loads, and boundary conditions used in analysis
Identify all materials and their properties
For thermal indicate the type of surfaces, insulation, and heaters that keep all subsystems within their allowable temperature ranges
  Create a table that identifies for all significant parts/assemblies the allowable temperature ranges in one column and the expected min/max temperature in the next column

## Slide 8: CDR Charts For Structures group
Show temperature contour plots of plate and solid parts for both hot and cold cases, clearly indicating max/min temperatures and where they occur on the part
For thermal analysis for part/subassembly represented by a node, create a table of all these parts/subassemblies showing the max/min temperatures and their allowable temperatures
Show transient temperature vs time plots where heaters are turned on and off to regulate temperature (i.e., show their duty cycle)

## Slide 9: CDR Charts For Controls group
Show controls analysis results
Clearly show controls schematics, assumptions, and calculations
Determine if any transient or overshoot occurs when CubeSat rotates to target
  Plot reaction wheel (RW) torque, CubeSat angular acceleration, angular velocity, and rotation vs time at sensor (IMU?) used to determine CubeSat position. Also, plot RW torque/angular velocity

## Slide 10: Dr. Brager (mentor) recommendations for CDR charts
The objective of CDR is for the stakeholders to have complete confidence that you are ready to begin implementing your proposed solution. So, all segments must be ‘on the same page’ and ready to go.
Project overview first identifying customer, stakeholders, state of need/objectives (describe the problem), system CONOP (concept of operations), and key SYSTEM requirements including overall size, weight, power, mission duration, orbit details, approvals required, etc. Also include a chart/table of how each requirement flows down to each segment. Also identify all funding sources and any conditions. Finally present Master Schedule with all segments identified and critical path clearly illustrated. Ensure all open action items are addressed.

## Slide 11: Dr. Brager (mentor) recommendations for CDR charts
Segment overviews: Begin with segment overview, illustration, stakeholders, etc. Present CONOP for the segment. Then identify all system requirements that flowed down in a table. Then add unique additional requirements related to the segment. Finally identify any requirements that the segment is levying on other segments or the overall system.
Present proposed solution and add a column in the requirements tables to show how the solution meets or exceeds each requirement and identify the margin. Clearly identify any requirement where the proposed solution does NOT meet the requirement and identify alternatives. Make sure to identify proposed vendors, order dates, and lead times for all budget items.
Make sure to identify critical path in the schedule (Gantt Chart) and include extra time (management reserve). For risks, identify proposed mitigation strategy to minimize each risk. Finally ensure that all prior action items are closed.